## Slide 1
Tutorial 13 Pipelined RISC-V
Maroun Tork, 2018

## Slide 2: Pipelined RISC-V RV32I Datapath
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
instM
instW
Must pipeline instruction (including Rd) along with data, so control operates correctly in each stage
Notes: Note that now we do not remove the computations modules (As we did in Multi-cycle), since all 3 computation modules are employed all the time.
Opcode (+some other fields) follows the instruction along the pipe
Which bits are sent – will discuss later, but note the RD field must be sent over to serve at WB stage
PC+4 is recalculated at MEM stage (where we may need PCC and PC+4), “PCC” is sent over the pipe

## Slide 3: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
IF/ID
ID/EX
EX/MEM
MEM/WB
add t0, t1, t2 or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
add t0, t1, t2
or t3, t4, t5

## Slide 4: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
IF/ID
ID/EX
EX/MEM
MEM/WB
add t0, t1, t2 or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3

## Slide 5: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
IF/ID
ID/EX
EX/MEM
MEM/WB
add t0, t1, t2 or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)

## Slide 6: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
IF/ID
ID/EX
EX/MEM
MEM/WB
add t0, t1, t2 or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)

## Slide 7
add t0, t1, t2
Time [Cycles]
Pipelined RISCV – Abstraction
or t3, t4, t5
Notes: Note: no hazard for LW.

## Slide 8
add t0, t1, t2
or t3, t4, t5
slt t6, t2, t1
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Time [Cycles]
Each stage operates on different instruction
Notes: Note: no hazard for LW.

## Slide 9: Pipelined RISC-V RV32I Datapath
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Notes: Note that now we do not remove the computations modules (As we did in Multi-cycle), since all 3 computation modules are employed all the time.
Opcode (+some other fields) follows the instruction along the pipe
Which bits are sent – will discuss later, but note the RD field must be sent over to serve at WB stage
PC+4 is recalculated at MEM stage (where we may need PCC and PC+4), “PCC” is sent over the pipe

## Slide 10: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation
  Information is stored in pipeline registers for use by later stages
Notes: Note the pipe-register names: IF/ID, etc.

## Slide 11: Data Hazard: Reminder
add t0, t1, t2
or t3, t4, t5
slt t6, t2, t1
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
There are more than one data hazard in this example, in this slide we focus only on t0
Notes: Does lw have Hazard? Answer: yes! But this time it’s not t0 (it’s t3, we will talk about it soon).

## Slide 12: RISC-V (RV32) Register File
2:1
2:1
Reg File Forward Logic
Rd
Rs1
To ALU
Rs2
RegWEnb
Forward within RF from DataIn to DataOut[1,2] when rd=rs[1,2] and RegWEnb=1
Notes: Add the wires, the two output muxes, and the decision logic

## Slide 13: Data Hazard: ALU Result
add t0, t1, t2
sub t2, t0, t5
or t6, t0, t3
instruction sequence
xor t5, t1, t0
sw t0, 8(t3)
Value of t0 in RF
Without some fix, sub and or will calculate wrong result!
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9

## Slide 14: Solution 1: Stalling
Problem: Instruction depends on result from previous instruction
  add t0, t1, t2 sub t2, t0, t5
Bubble: effectively NOP – do “nothing”
add t0, t1, t2
  sub t2, t0, t5
Notes: Ask the students:
How do we implement NOP?

## Slide 15: Solution 2: Forwarding
add t0, t1, t2
sub t2, t0, t5
or t6, t0, t3
instruction sequence
xor t5, t1, t0
sw t0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of t0 in RF
Forwarding: grab operand from pipeline stage, rather than register file.

## Slide 16: Forwarding Paths
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Forwarding Control Logic
Notes: MEM and WB stages pass over to Forward Control logic the information on destination register Rd and the RegWEnb control signal (in order to indicate whether write-RF is enabled). This data is compared to RS1 and RS2 of the instruction currently in EX stage.

## Slide 17: Load Data Hazard
Cannot be forwarded

## Slide 18
Load Data Hazard
Solution: Hazard Detection Unit Inserts Bubble after LW in case of Load Data hazard

## Slide 19
How to Stall the Pipeline
Example: Load is Decoded (1/4)
Notes: IF/IDWrite – an additional control line of enable for IF/ID register (keeps here the register from loading the new value from IF).

## Slide 20
How to Stall the Pipeline
Example: Load Hazard is Detected (2/4)
Notes: Here we detect the hazard and set control lines to issue bubble towards EXE stage on the next cycle.

## Slide 21
How to Stall the Pipeline
Example: Bubble Inserted (3/4)

## Slide 22
How to Stall the Pipeline
Example: Data Gets Forwarded (4/4)
Notes: Here we forward $2 from WB stage to EXE.

## Slide 23: Control Hazards
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
xor t5, t1, s0
sw s0, 8(t3)
executed regardless of branch outcome!
executed regardless of branch outcome!
PC updated reflecting branch outcome

## Slide 24: Solution
If branch not taken, then instructions fetched sequentially after branch are correct
If branch or jump is taken, then need to flush incorrect instructions from pipeline by converting to NOPs

## Slide 25: Kill Instructions after Branch if Taken
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
label: xxxxxx
PC updated reflecting branch outcome
Taken branch
Convert to NOP
Convert to NOP

## Slide 26
שאלות?

## Slide 27
שאלה 1 – אביב תשע"ט מועד א'

## Slide 28
LW כותב ל- רגיסטר s1, ו- addi קורא ממנו. יחידת ה Hazard Detection תוסיף Bubble בין הפקודות ויחידת ה- Forwarding תעביר את הערך מה- WB ל- EXE
5
S1
WB
Exe
באותו מחזור, נשים לב שמעבירים את S1, גם לפקודת sub
5
S1
WB
Decode

## Slide 29
5
S1
WB
Exe
5
S1
WB
Decode
6
S0
Mem
Exe
מחזור לאחר מכן, כשפקודת ה- addi, תגיע לשלב ה- Mem, ערך S0 יועבר ל- sub שנמצא בשלב ה- Exe
גם פקודת ה- SW קוראת את s0, ולכן כש- addi תגיע ל- WB ערך S0 יועבר גם אליה
7
S0
WB
Exe

## Slide 30
5
S1
WB
Exe
5
S1
WB
Decode
6
S0
Mem
Exe
באותו מחזור, כש- SUB נמצאת ב- Mem, ערך S1 יועבר מ- SUB ל- SW
7
S0
WB
Exe
7
S1
Mem
Exe

## Slide 31
שאלה 2א – חורף תשע"ט מועד א'

## Slide 32
WB
Decode
אין Forwarding ברגיסטר פייל! נצטרך לפחות NOP בין הפקודות
יש Forwarding בין ה-WB ל- Execute, ולכן לא נצטרך לשים NOP בין הפקודות.

## Slide 33
NOP
כשה- Branch לא נלקח בפעם הראשונה, יש Hazard בין הפקודות האלה, שלא מטופל כי אין Forwarding בין ה- WB ל- Decode. נצטרך לשים NOP גם ביניהם.
הוספת ה- NOP מונעת את שני ה- Hazard שציינו אבל יוצרת Hazard חדש
אז נצטרך להוסיף שתי פקודות NOP
; NOP

## Slide 34
NOP x 2
אין Hazard Detection Unit, ולכן נצטרך להוסיף NOP מיד לאחר ה- LW
NOP
בסה"כ נצטרך להוסיף 3 NOP

## Slide 35
שאלה 2ב – חורף תשע"ט מועד א'

## Slide 36
ללא מנגנון ה- Prediction, המעבד מניח שפקודת ה- Branch אינה נלקחת ועושה Flush ל- Pipe במידה וכן
ה- Branch הראשון לא נלקח 5 פעמים, ונלקח פעם אחת
ה- Branch השני נלקח 5 פעמים
סה"כ 5 Branch לא נלקחים, ו- 6 נלקחים. כלומר, במצב הנתון, לא נצטרך לבצע Flush ל- Pipe עבור 5 קפיצות מתוך 11 קפיצות. לכן אם המנגנון יצדק יותר מ- 5/11 פעמים נבחר להשתמש בו.

## Slide 37
שאלה 3א – חורף תשע"ט מועד ב' (גרסה מתוקנת ומורחבת)
נתון מעבד Pipelined RISC-V כפי שנלמד בתרגול

## Slide 38
סעיף חימום (לא הופיע במבחן) – בהינתן הקוד להלן, מה המספר המינימלי של פקודות NOP שנצטרך להוסיף בין הפקודות כדי שהקוד ירוץ כשורה?
LW t1, 0(s1)
SW t2, 0(t1)

## Slide 39
שנית, נדע את ערך t1 רק לאחר שלב ה- Mem, בזמן שפקודת ה- SW תהיה בשלב ה- Mem. אין לנו Forwarding משלב ה- WB לשלב ה- Mem ולכן נצטרך להוסיף בשלב הראשון פקודת NOP אחת.
ראשית, נשים לב ש LW כותב ל- t1, ו- SW קורא ממנו.
LW t1, 0(s1)
SW t2, 0(t1)
בשלב הבא, יש לנו Forwarding משלב ה- WB לשלב ה- Execute, ספציפית לתוך הקלט העליון של ה- ALU, ולא נצטרך להוסיף עוד NOPs.
סה"כ נצטרך פקודת NOP אחת

## Slide 40
שאלה 3ב – חורף תשע"ט מועד ב' (גרסה מתוקנת ומורחבת)

## Slide 41
ראשית, נשים לב ש LW כותב ל- t1, ו- SW קורא ממנו.
שנית, נדע את ערך t1 רק לאחר שלב ה- Mem, בזמן שפקודת ה- SW תהיה בשלב ה- Mem. אין לנו Forwarding משלב ה- WB לשלב ה- Mem ולכן נצטרך להוסיף בשלב הראשון פקודת NOP אחת.
כעת נשים לב שיחידת ה- Forwarding כלל לא רלוונטית במקרה זה, משום שהערך שמועבר בין שלב ה- WB לשלב ה- EXE מתבצע הוא ערך ה- Addr לזיכרון, ולא ה- Data ולכן נצטרך להוסיף NOP נוסף.

## Slide 42
לבסוף נתון שה- RegFile לא מכיל Forwarding, ולכן נצטרך להוסיף NOP שלישי.
סה"כ נפריד לחלוטין בין שתי הפקודות ע"י 3 פקודות NOP.

## Slide 43
שאלה 3ג – חורף תשע"ט מועד ב' (גרסה מתוקנת ומורחבת)
סעיף ג' (לא הופיע במבחן)
הצע תיקון ל- Datapath ע"י הוספת / שינוי חוטים ובוררים על מנת להפחית את כמות פקודות ה- NOP הנדרשות. כמה פקודות NOP נדרשות כעת?

## Slide 44
ע"י הוספת Forwarding משלב ה- WB לשלב ה- MEM (לתוך כניסת ה- DATA של ה- DMEM)

## Slide 45
שאלה 4 – אביב תשע"ט מועד ב'
נתון קוד המבצע מכפלה סלקרית בין וקטורים השמורים כמערכים בזיכרון.

## Slide 46
שאלה 4 – אביב תשע"ט מועד ב'
זמן המחזור ע"ג מעבד Single Cycle הוא סכום חלקי המעבד – 1000ns. מספר הפקודות שהמעבד יריץ הוא: 10 פעמים את 9 הפקודות שבגוף הלולאה, ועוד פקודה אחת לפני ופקודה אחת אחרי הלולאה. סה"כ – 90 + 2 = 92 פקודות. זמן הריצה הינו:

## Slide 47
שאלה 4 – אביב תשע"ט מועד ב'
איפה המהנדס ייאלץ להוסיף פקודות NOP על מנת שהקוד ירוץ כשורה על המעבד?
בין פקודה 3 לפקודה 4 נצטרך להוסיף 2 פקודות NOP משום שאין Hazard Detection, ואין יחידת Forwarding (יש Forwarding ב- Regfile ולכן רק 2).
בין פקודה 4 ל- 5 נצטרך להוסיף 2 פקודות NOP נוספות (אין Forwarding)
בין פקודה 9 ל- 10 נצטרך להוסיף 2 פקודות NOP נוספות (אין Forwarding)

## Slide 48
שאלה 4 – אביב תשע"ט מועד ב'
ניתן לשנות את סדר הפקודות כך שמספר פקודות ה- NOP יפתח. למשל, העברת פקודה 6, לבין פקודות 3 ו- 4 (פתרון אופטימלי (אינו נדרש במבחן) ללא פקודות NOP כלל בשקף הבא)

## Slide 49
שאלה 4 – אביב תשע"ט מועד ב'

## Slide 50
שאלה 4 – אביב תשע"ט מועד ב'
ללא פקודות NOP כלל, 4 מחזורים ראשונים ידרשו למילוי ה- Pipe (כשלאחר המילוי כל חלקי ה- Pipe יהיו מלאים). לאחר מכן בכל מחזור תסתיים פקודה. נשים לב שהמעבד מניח שפקודת ה- BNE אינה נלקחת, ומבצע Flush של 2 פקודות בכל ריצת הלולאה חוץ מאשר בריצה האחרונה של הלולאה.
בסה"כ מספר המחזורים הינו – 4+1+ 9*(9+2)+1*(10)=5+99+10=114
זמן המחזור נקבע לפי החלק הארוך ביותר במעבד, ולכן – T=300ns
בסה"כ זמן הריצה על המעבד הינו – 114 * 300ns =