## Slide 1: SystemVerilog HDL Workshop #1
044252 - Digital Systems and Computer Structure

## Slide 2: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 3: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 4
Logic Gates – A Reminder

## Slide 5: Ways to Represent Hardware:
Hardware Description Language
Netlist
Schematic drawing
Truth table
nand(Z, X, Y);
logic Z;
assign Z = X ~& Y;
logic Z;
always_comb
if (X) Z = ~Y;
else Z = 1;
X | Y | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 6: Hardware Description Languages (HDLs)
Textual representation of digital circuits
HDLs are not “programming languages”
  No, really. Even if they look like it, they are not.
Similar development chain to software
  Software: Compiler
    Source code  Assembly code  Machine code
  Hardware: Synthesizer
    HDL Source  Netlist  Hardware

## Slide 7: Why Use an HDL?
Easy to write and edit
Compact
Don’t have to follow a maze of lines
Easy to analyze with various tools

## Slide 8: SystemVerilog
Superset of Verilog
One of the two leading HDLs - VHDL is the other.
Most digital chips are designed in part using one of these two languages

## Slide 9: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 10: Modules
module: fundamental building block
  Describes a digital circuit
  Hierarchical modules contain (instantiate) other modules
f
in1
in2
inN
out1
out2
outM
my_module
Everything you write in SystemVerilog must be inside a module!

## Slide 11: Modules
module my_module(
output logic out1,
output logic out2,
...,
input logic inN
);
... // declarations
... // description of f
endmodule
Module Name
Input and Output Declaration
f
in1
in2
inN
out1
out2
outM
my_module
No ; !
Module Start & End

## Slide 12: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 13: The Logic Data Type
The logic data type represents a wire (1 bit)
Declaring a logic variable:
a
b
c
d
e
logic a, b, c, d; logic e;

## Slide 14: The Logic Data Type
In this course, we will use the logic data type
More data types in SystemVerilog (not recommended!)
  wire
  reg
  integer
  time
  More…
logic type replaces both wire and reg

## Slide 15: SystemVerilog Logic Values
0: zero / logic low / false / ground
1: one / logic high / true / power
x: not initialized or collision
z: unconnected

## Slide 16: Reminder: 41 Selector /Multiplexer / Mux
Input: | 2 Control inputs
 | 22 Data inputs
 | Enable input
Output: | if E=0 then ‘0’
 | else DS
E
How to represent several bits?
O

## Slide 17: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 18: Vectors
Declaration of an 8-bit logic vector:
Exercise: write a mux module declaration
logic [7:0] w1; // w1[7] is the MSB
O

## Slide 19: Mux Module Declaration - Solution
module mux4to1(
output logic O,
input logic D0,
input logic D1,
input logic D2,
input logic D3,
input logic E,
input logic [1:0] S
);
... // declarations
... // description of a mux
endmodule
O

## Slide 20: Vector Operations
  Bit select:
  Range select:
  Pack:
  Unpack:
vec = {x, y, z};
{carry, sum} = vec[1:0];
w1[3]
w1[3:2]

## Slide 21: Vectors - Exercise
Swap high and low nibbles of w1 into w2
Solution:
logic [7:0] w1; logic [7:0] w2;
w2 = {w1[3:0], w1[7:4]};

## Slide 22: Intro – 2’s complement
N-bit Unsigned binary:
N-bit Signed binary:
The only difference is the MSB changes to a negative value!
Example: 1010 Example: 11010
Unsigned: 8+2 = 10 Unsigned: 16+8+2 = 26
Signed: -8+2 = -6 Signed: -16+8+1 = -6

## Slide 23: Repeated Signals
Previously we discussed vector concatenation:
We can also repeat a signal n times:
vec = {x, y, z};
vec = {16{x}}; // 16 copies of x

## Slide 24: Repeated Signals - Example
Question: What does this do?
Answer: Unsigned extension
Question: What about this?
Answer: Signed extension
logic [7:0] out; logic [3:0] A; out = {{4{0}}, A[3:0]};
out = {{4{A[3]}}, A[3:0]};

## Slide 25: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 26: Module Implementation
There are 3 ways to implement hardware inside a module:
  Module instantiation
  Concurrent assignments
  Procedural blocks

## Slide 27: Module Instantiation
Implementing a module using other modules as building blocks
My Module
Module
Building Block #1
Module
Building Block #2
input1
output1

## Slide 28: Module Instantiation
Implementing a module using other modules as building blocks

## Slide 29: Module Instantiation Syntax
module_name instance_name1 (
my_out1,
my_out2,
...,
my_inN
);
Positional association:
Named association:
module_name instance_name2 (
.out1(my_out1),
.out2(my_out2),
...,
.inN(my_in1)
);
044252 - Digital Systems and Computer Structure - SystemVerilog HDL Workshop
29
Instance name
Input and Output port assignments
Module name
Module port name
Wire name
Module name
Instance name

## Slide 30: Module Instantiation Example
top
mymodule
A
B
C
mymodule
A
B
C
inst1
inst2
net1
net2
net3
net4
net5
module mymodule (
output logic C,
input logic A,
input logic B
);
…
…
endmodule
module top;
logic net1, net2, net3, net4, net5;
…
mymodule inst1 (net4, net1, net2);
mymodule inst2 (.C(net5), .A(net2), .B(net3));
…
endmodule
Connect by name
Use this only!
Connect by position

## Slide 31: Built-in SystemVerilog Modules
Basic logic gates available for direct instantiation
  and
  or
  not
  xor
  nand
  nor
  xnor
Syntax: gateName(output, input1, <input2>)
not(O1, A);
nor(O2, A, B);

## Slide 32: Example – Half Adder Implementation

## Slide 33
module HA (
output logic S,
output logic C,
input logic A,
input logic B
);
xor(S, A, B);
and(C, A, B);
endmodule
Example – Half Adder Implementation

## Slide 34: Module Instantiation Example
What we have:
What we need:
A[1:0]
B[1:0]
Build complex modules using simpler modules
S
S
O
O[1:0]

## Slide 35: Module Instantiation Example
2-bit wide mux from two 1-bit muxes
  Just “drawing” boxes and wires
  module mux2to1_2 (
  output logic [1:0] O,
  input logic [1:0] A,
  input logic [1:0] B,
  input logic S
  );
  mux2to1 mux0 (.O(O[0]), .S(S), .A(A[0]), .B(B[0]));
  mux2to1 mux1 (.O(O[1]), .S(S), .A(A[1]), .B(B[1]));
  endmodule
Module Name
Instance Name
Input Port Name
Input Port Assignment
B[1:0]
S
O[1:0]
A[1:0]
A]0[
B]0[
A]1[
B]1[
O]0[
O]1[
O
O
S
S

## Slide 36: The generate Command
Implementation of a 32-bit wide mux from 32 1-bit muxes using regular instantiation is long and exhausting…
  Use generate
module mux2to1_32 (
output logic [31:0] O, // Output bits O
input logic [31:0] A, // Input bits A
input logic [31:0] B, // Input bits B
input logic S // Select
);
genvar i;
generate
for (i = 0; i < 32; i++)
begin
mux2to1 mux_inst(.O(O[i]), .S(S),
.A(A[i]), .B(B[i]));
end
endgenerate
endmodule

## Slide 37: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 38: SystemVerilog: design vs. simulation
Simulation = a way to test the design
Initial begin
#1 a = 1;
#3 b = 1;
#5 a = 0;
…
end

## Slide 39: How Are Simulators Used?
Testbench generates stimuli and checks response
Testbench
Response
Module Instance
(UUT)
.
.
.
InputN
Input1
.
.
.
OutputM
Output1
Stimuli

## Slide 40: Test Bench - Generating Stimuli
Data: A sequence of values
initial begin
data = 0;
#50
data = 1;
#30
data = 0;
#20
data = 1;
end

## Slide 41: Test Bench
module HA_tb;
logic ha_a;
logic ha_b;
logic ha_sum;
logic ha_carry;
HA uut (
.a(ha_a),
.b(ha_b),
.sum(ha_sum),
.carry(ha_carry)
);
initial begin
ha_a = 0;
ha_b = 0;
20#
ha_a = 1;
ha_b = 0;
20#
ha_a = 0;
ha_b = 1;
20#
ha_a = 1;
ha_b = 1;
end
endmodule
Stimuli Signals Creation
Tested Module Instantiation
Stimuli Generation
Testbench
Module Instance
(UUT)
.
.
.
InputN
Input1
.
.
.
OutputM
Output1
Stimuli

## Slide 42: Mux Implementation using a Decoder

## Slide 43: Full Adder Implementation using Two Half Adders

## Slide 44: Wet Exercise 0
You will be required to:
  Get to know ModelSim
  Fix bugs in a HA implementation
  Test it using a simulation
The videos are recommended
The workshops cover all the syntax needed to solve the wet exercise

## Slide 45: Workshop #1 Cheat Sheet
Module:
Logic:
Logic values: 0, 1, x, z
Vector:
module my_module(
output logic ...,
input logic ...
);
... // declarations
... // description of a mux
endmodule
logic a, b, c, d;
logic [7:0] w1; // w1[7] is the MSB

## Slide 46: Workshop #1 Cheat Sheet
Vector operations:
  Bit select
  Range select
  Pack
  Unpack
  Repeated signals
vec = {x, y, z};
{carry, sum} = vec[1:0];
w1[3]
w1[3:2]
vec = {16{x}}; // 16 copies of x

## Slide 47: Workshop #1 Cheat Sheet
Module instantiation:
Built-in logic gates:
module_name instance_name1 (
.out1(my_out1),
.out2(my_out2),
...,
.inN(my_in1)
);
not(O1, A);
nor(O2, A, B);

## Slide 48: Workshop #1 Cheat Sheet
Generate:
genvar i;
generate
for (i = 0; i < 32; i++)
begin
mux2to1 mux_inst(.out(O[i]), .sel(sel),
.A(A[i]), .B(B[i]));
end
endgenerate

## Slide 49: Questions?