## Slide 1: SystemVerilog HDL Workshop #3
044252 - Digital Systems and Computer Structure

## Slide 2: Topics Covered Last Time
Hardware Description Languages
SystemVerilog Building Blocks:
  Values / Number representation
  Bitwise operators
  Module implementation
    Module instantiation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Test benches and simulation

## Slide 3: Topics Covered Last Time
Hardware Description Languages
SystemVerilog Building Blocks:
  Values / Number representation
  Bitwise operators
  Module implementation
    Module instantiation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Test benches and simulation

## Slide 4: Module Instantiation - Recap
2-bit wide mux from two 1-bit muxes
  module mux2to1_2 (
  output logic [1:0] O,
  input logic [1:0] A,
  input logic [1:0] B,
  input logic sel
  );
  mux2to1 mux0 (.out(O[0]), .sel(sel), .A(A[0]), .B(B[0]));
  mux2to1 mux1 (.out(O[1]), .sel(sel), .A(A[1]), .B(B[1]));
  endmodule
B[1:0]
sel
O[1:0]
A[1:0]
A]0[
B]0[
A]1[
B]1[

## Slide 5: Concurrent Assignments - Recap
Connect a wire to a combinational logic or another wire
When the right-hand-side of an assignment changes, it immediately flows through to the left-hand-side wire
Syntax:
logic signal;
assign signal = 1'b0;
logic signal1;
logic signal2;
assign signal2 = signal1;

## Slide 6: Procedural Blocks - Recap
Sequential: all statements inside the block are executed sequentially
  One line after the other
Two procedural constructs:
initial begin
<statement1>;
# time_to_wait
<statement2>;
# time_to_wait
...
end
always_comb begin
<statement1>;
<statement2>;
...
end
initial:
always_comb:

## Slide 7: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 8: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 9: Relational Operators
All of these return a 1-bit logical value (true/false or ‘x’)
Meaning | Operator
Less than | <
Less than or equal to | <=
Greater than | >
Greater than or equal to | >=
Equal to | ==
Not equal to | !=

## Slide 10: Logical Operators
Used for conditions
Operands evaluated to 1-bit value: 0 (false), 1 (true) or x
Result is 1-bit value: 0 (false), 1 (true) or x
Meaning | Operator
Logical AND | &&
Logical OR | ¦¦
Logical NOT | !

## Slide 11: Logical Operators
logic A, B, C;
assign A = 1'b1;
assign B = 1'b0;
assign C = 1'bx;
Examples:
false | true && false  | A && B 
true | true ¦¦ true  | A ¦¦ !B 
x | x ¦¦ false  | C ¦¦ B 
false | x && false  | C && B 

## Slide 12: SystemVerilog Operator Precedence

## Slide 13: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 14: Conditional Statements: The if Statement
Used in procedural blocks
Syntax:
if (condition1) begin
<statement1>;
end
else if (condition2) begin
<statement2>;
end
else begin
<statement3>;
<statement4>;
end

## Slide 15: The if Statement - Example
Mux Module:
A
B
Q
sel
module mux (
input logic A,
input logic B,
input logic sel,
output logic Q
;(
always_comb begin
if (sel == 1'b0) begin
Q = A;
end
else begin
Q = B;
end
end
endmodule
0
1

## Slide 16: Reminder: Mux Implementation
module mux (
output logic out,
output logic outn,
input logic [1:0] in,
input logic sel
);
logic out1, out2, selb;
and a1 (out1, in[0], sel);
not i1 (selb, sel);
and a2 (out2, in[1] , selb);
always_comb begin
out = out1 | out2;
end
assign outn = ~out;
endmodule
in
2
In[0]
In[1]
outn

## Slide 17: Conditional Statements: The case Statement
Used in procedural blocks
Syntax:
case (<signal/expression>)
<value1>: begin
<statement1>;
end
  <value2>: begin
  <statement2>;
  <statement3>;
  end
default: begin
<statement4>;
end
endcase

## Slide 18: The case Statement - Example
module case_example (
input logic A,
input logic B,
input logic [1:0] w,
output logic Y
;(
always_comb begin
case (w)
2'b00: Y = A & B;
2'b01: Y = A | B;
2'b10: Y = A ^ B;
default: Y = ~B;
endcase
end
endmodule
A
B
Y
w
00
2
01
10
11

## Slide 19: Conditional Statements: casex, casez
Variants of case Statements:
  casex and casez
casez – ? and z are considered as don’t cares [0,1,z]
casex – ?, x and z are considered as don’t cares [0,1,x,z]
Example:
casez(w)
2'b1?: A = B + C;
2'b01: A = B ^ C;
default: A = B – C;
endcase

## Slide 20: A Not-To-Do Example
module bad_mux (
input logic A,
input logic B,
input logic sel,
output logic Q
;(
always_comb begin
if (sel == 1'b1) begin
Q = A;
end
end
endmodule
A
Q
sel
G
I
O
Latch

## Slide 21: Complete Assignments
always_comb should NOT be used for memory elements!
  If a signal is not assigned in a certain flow, a memory element is implicitly created to preserve the previous value
  Usually, this is a bug!
When using always_comb, always use complete assignments, i.e., assign values to all signals in all logic flows!

## Slide 22: Complete Assignments: Guidelines
“if” statements
  Use “else”
“case” statements
  Use “default”
General solution
  Use default assignments
always_comb begin
Q = 1'b0;
if (sel == 1'b1) begin
Q = A;
end
end
‘0’
A
sel
0
1
Q

## Slide 23: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 24: Flip Flop: Reminder

## Slide 25: The always_ff Statement
always_comb: implements an asynchronous/ combinatorical block
always_ff: implements a synchronous block
clk

## Slide 26: The always_ff Statement (without Reset)
Syntax:
always_ff @(posedge clk) begin
<sync statement1>;
<sync statement2>;
end
Sensitivity List
Sync Statements (on clock rise)

## Slide 27: always_ff Example: Implementing a Flip-Flop
logic a, in;
always_ff @(posedge clk) begin
a <= in;
end
clk
in
a
‘1’
‘0’
‘0’

## Slide 28: The always_ff Statement with Reset
Syntax:
always_ff @(posedge clk) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
With Synchronous Reset:
Initialization Statements (on reset)
Sensitivity List (no reset!)
Sync Statements (on clock rise)
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
With Asynchronous Reset:
Initialization Statements (on reset)
Sensitivity List
Sync Statements (on clock rise)

## Slide 29: always_ff Example: Implementing a Flip-Flop with Reset
logic a, in;
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
a <= 1'b0;
end
else begin
a <= in;
end
end
rst
clk
in
a
‘1’
‘0’

## Slide 30: Assignment in an always_ff Block
In always_comb, we use a blocking assignment (= operator):
In always_ff, we use a non-blocking assignment (<= operator):
logic a, in;
always_comb begin
a = in;
end
logic a, in;
always_ff @(posedge clk) begin
a <= in;
end

## Slide 31: Procedural Assignments
Occur within procedural blocks such as always_comb, always_ff and initial
Triggered when the flow of execution reaches them
Blocking/Non-blocking
  Blocking assignment statement (= operator) acts much like in traditional programming languages. The whole statement is done before control passes on to the next statement
  Non-blocking assignment statement (<= operator) evaluates all the right-hand sides for the current time unit and assigns the left-hand sides at the end of the procedural block

## Slide 32: Example – Non blocking
module shifter(
input logic in,
input logic clk
;(
logic A, B, C;
always_ff @(posedge clk) begin
A <= in;
B <= A;
C <= B;
end
endmodule
A
clk
in
B
C

## Slide 33: Example – Blocking
module bad_shifter(
input logic in,
input logic clk
;(
logic A, B, C;
always_ff @(posedge clk) begin
A = in;
B = A;
C = B;
end
endmodule
B
C
A
clk
in

## Slide 34: Assignment Summary
Synchronous logic: Use non-blocking statements with always_ff blocks sensitive only to rising clock edge to mimic parallel synchronous logic.
Combinational logic: Use blocking statements inside always_comb blocks with to mimic logic flow of combinational logic.

## Slide 35: Assignment: A Question From an Exam (Winter '18-'19)

## Slide 36: Example: Synchronous and Asynchronous Logic
A
clk
B
or_out
and_out
Synchronous Logic
Asynchronous/Combinatorical Logic
rst
A
A
B

## Slide 37: Example: Sync. and Async. Logic
module my_module (
input logic clk,
input logic rst,
output logic A,
output logic B
;(
  logic and_out, or_out;
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= or_out;
  B <= and_out;
  end
  end
  always_comb begin
  and_out = A & B;
  or_out = A | B;
  end
endmodule
Asynchronous/Combinatorical Logic
Synchronous Logic

## Slide 38: Example: Sync. and Async. Logic: Another Implementation
module my_module (
input logic clk,
input logic rst,
output logic A,
output logic B
;(
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= A | B;
  B <= A & B;
  end
  end
endmodule
Asynchronous &
Synchronous Logic

## Slide 39: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 40: Test Bench: Generating a Clock Signal
initial begin
Clock = 1'b0;
end
...
always begin
#10 Clock = ~Clock;
end
Clock
always statement: runs in an endless loop

## Slide 41: Test Bench: The Repeat Loop
  Used in an initial block to repeat statements.
  Syntax:
  Example: Waiting for 4 clock cycles
initial begin
repeat(4) begin
@(posedge clk);
end
end
repeat(num_of_times) begin
<statement1>;
<statement2>;
end

## Slide 42: Test Bench: Full Example
module my_module_tb;
logic clk, rst;
logic A, B;
my_module inst(.clk(clk), .rst(rst), .A(A), .B(B));
always begin
#10 clk = ~clk;
end
initial begin
clk = 1'b0;
rst = 1'b1;
@(posedge clk);
7#
rst = 1'b0;
repeat(2) begin
@(posedge clk);
end
end
endmodule

## Slide 43: Test Bench: Full Example

## Slide 44: Another Example: Simple Counter
current_counter
clk
next_counter
+1

## Slide 45: Another Example: Simple Counter
logic [3:0] next_counter, current_counter;
always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  current_counter <= 4'b0;
  end
  else begin
  current_counter <= next_counter;
  end
end
always_comb begin
next_counter = current_counter + 1;
end
current_counter
clk
next_counter
+1

## Slide 46: Another Example: Simple Counter
logic [3:0] current_counter;
always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  current_counter <= 4'b0;
  end
  else begin
  current_counter <= current_counter + 1;
  end
end
current_counter
clk
+1

## Slide 47: A Question From an Exam (Spring '19)

## Slide 49: Workshop #3 Cheat Sheet
Logical operators: &&, ||, !
Relational operators: >, >=, <, <=, ==, !=
if statement:
if (condition1) begin
<statement1>;
end
else if (condition2) begin
<statement2>;
end
else begin
<statement3>;
<statement4>;
end

## Slide 50: Workshop #3 Cheat Sheet
case statement:
casez: ? and z are considered as don’t cares [0,1,z]
casex: ?, z and x are considered as don’t cares [0,1,z,x]
case (<signal/expression>)
<value1>: begin
<statement1>;
end
  <value2>: begin
  <statement2>;
  <statement3>;
  end
default: begin
<statement4>;
end
endcase

## Slide 51: Workshop #3 Cheat Sheet
always_ff statement:
always_ff with reset:
Async. Reset: Sync. Reset:
always_ff @(posedge clk) begin
<sync statement1>;
<sync statement2>;
end
always_ff @(posedge clk) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end

## Slide 52: Workshop #3 Cheat Sheet
Generating a clock signal:
repeat loop:
repeat(num_of_times) begin
<statement1>;
<statement2>;
end
initial begin
Clock = 0;
end
...
always begin
#10 Clock = ~Clock;
end

## Slide 53: Questions?