## Slide 1: SystemVerilog HDL Workshop #4
044252 - Digital Systems and Computer Structure

## Slide 2: Agenda
enum
FSM design in SystemVerilog
FSM code examples

## Slide 3: Agenda
enum
FSM design in SystemVerilog
FSM code examples

## Slide 4: enum
An enum type defines a set of named values
Syntax:
Example:
We will use enum for state declaration:
typedef enum {name1, name2, name3} set_name;
typedef enum {red, green, blue} color_type;
color_type c;
typedef enum {idle_st, state1, state2} state_type;

## Slide 5: Agenda
enum
FSM design in SystemVerilog
FSM code examples

## Slide 6: Reminder – What is FSM?

## Slide 7: FSM – Writing Code
Declare states used for FSM
Write FSM using two procedural blocks:
  Synchronous – saves current state
  Asynchronous – sets next state and output signals (according to current state and optionally input signals)
Other helper procedural blocks can also be used

## Slide 8: FSM Template
module my_FSM_module (
input logic input1,
...
output logic outputN
;(
// Declaring the FSM states
typedef enum { idle_st, start_st } sm_type;
// Declaring signals for the next & current state
sm_type current_state;
sm_type next_state;
// ...
endmodule

## Slide 9: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 10: FSM – Async Logic
always_comb begin
next_state = current_state;
output1 = 1'b0;
...
outputN = 1'b0;
case (current_state)
idle_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
start_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
...
endcase
end
Default Assignments

## Slide 11: Agenda
enum
FSM design in SystemVerilog
FSM code examples

## Slide 12: FSM Example – Edge Detector
Requirements:
  Mealy FSM
  Receives several signals:
    clk
    rst (asynchronous)
    level
  Outputs a signal called tick
  When the level signal changes from ‘0’ to ‘1’, the tick signal is ‘1’ in this clock cycle. Else, the tick signal is ‘0’.

## Slide 13: Edge Detector: FSM Design
Zero state
One state
level == ‘1’ /
tick = ‘1’
level == ‘0’ /
tick = ‘0’
level == ‘0’ /
tick = ‘0’
level == ‘1’ /
tick = ‘0’
rst

## Slide 14: FSM: Top Level and Signal Declarations
module edge_detector (
input logic clk,
input logic rst,
input logic level,
output logic tick
;(
// Signal declarations
typedef enum { zero_st, one_st } sm_type;
sm_type current_state;
sm_type next_state;
...
endmodule

## Slide 15: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= zero_st; end else begin current_state <= next_state; end end

## Slide 16: FSM – Async Logic
always_comb begin next_state = current_state; tick = 1'b0; case (current_state) zero_st: begin if (level == 1'b1) begin next_state = one_st; tick = 1'b1; end end one_st: begin if (level == 1'b0) begin next_state = zero_st; end end endcase end
Default assignment

## Slide 17: FSM Example – Vending Machine
Requirements:
  Mealy FSM
  Receives several signals:
    clk
    rst (asynchronous)
    coin_in: a 5 shekel coin is put into the machine.
    cancel: cancel the operation and return change.
  Outputs several signals:
    can_out: a can is brought out of the machine.
    coin_out: a coin is returned.
  The machine gets only 5 shekel coins. The price of a can is 10 shekels. When the total sum is put into the machine (two coins), the can_out signal rises.
  If the operation is canceled after one coin was inserted, the coin_out signal rises.
  All inputs and outputs are 1 clock cycle pulses.

## Slide 18: Vending Machine: FSM Design
Idle
Single coin state
coin_in == 1 && cancel == 0 /
can_out = 0
coin_out = 0
rst
coin_in == 0 && cancel == 1 /
can_out = 0
coin_out = 1
coin_in == 0 /
can_out=0
coin_out = 0
(coin_in == 0 && cancel == 0) / can_out = 0
coin_out = 0
coin_in == 1 && cancel == 0 /
can_out = 1
coin_out = 0
(coin_in == 1 && cancel == 1) /
can_out = 0
coin_out = 1
(coin_in == 1 && cancel == 1) /
can_out = 0
coin_out = 1

## Slide 19: FSM: Top Level and Signal Declarations
module vending_machine (
input logic clk,
input logic rst,
input logic coin_in,
input logic cancel,
output logic can_out,
output logic coin_out
;(
// Signal declarations
typedef enum { idle_st, single_coin_st } sm_type;
sm_type current_state;
sm_type next_state;
...
endmodule

## Slide 20: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 21: FSM – Async Logic
always_comb begin next_state = current_state; can_out = 1'b0; coin_out = 1'b0; case (current_state) idle_st: begin if ((coin_in == 1'b1) && (cancel == 1'b0)) begin next_state = single_coin_st; end else if ((coin_in == 1’b1) && (cancel == 1’b1)) begin coin_out = 1'b1; end end single_coin_st: begin if ((coin_in == 1’b0) && (cancel == 1'b1)) begin next_state = idle_st; coin_out = 1'b1; end else if ((coin_in == 1’b1) && (cancel == 1’b0)) begin next_state = idle_st; can_out = 1'b1; end else if ((coin_in == 1’b1) && (cancel == 1’b1)) begin coin_out = 1'b1; end end endcase end
Default assignment

## Slide 22: FSM Example – Clock Divider
Requirements:
  Moore FSM
  Receives several signals:
    clk
    rst (asynchronous)
  Outputs only one signal:
    q: the divided clock
  The machine outputs ‘0’ when the rst signal is high. Otherwise, it divides the clock frequency by 3. The duty cycle is 1/3.

## Slide 23: Clock Divider: FSM Design
S0
-----------
q=0
S1
-----------
q=0
rst
S2
-----------
q=1

## Slide 24: FSM: Top Level and Signal Declarations
module clock_divider ( input logic clk, input logic rst, output logic q ;( // Signal declarations typedef enum { S0_st, S1_st, S2_st } sm_type; sm_type current_state; sm_type next_state; ... endmodule

## Slide 25: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= S0_st; end else begin current_state <= next_state; end end

## Slide 26: FSM – Async Logic
always_comb begin case (current_state) S0_st: begin next_state = S1_st; q = 1'b0; end S1_st: begin next_state = S2_st; q = 1'b0; end S2_st: begin next_state = S0_st; q = 1'b1; end default: begin next_state = S0_st; q = 1'b0; end endcase end

## Slide 27: FSM Example – Parking Lot
Requirements:
  Moore FSM
  Receives several signals:
    clk
    rst (asynchronous)
    car_entering: ‘1’ if a new car enters the parking lot, ‘0’ otherwise.
    car_exiting: ‘1’ if a car exits the parking lot, ‘0’ otherwise.
    N (parameter): maximum limit
  Outputs only one signal:
    gate_open: ‘1’ when there is room for a car, ‘0’ else.

## Slide 28: Parking Lot: High-Level Design
FSM
Counter
counter
car_entering
car_exiting
gate_open

## Slide 29: Parking Lot: FSM Design
Open
--------------
gate_open = ‘1’
Closed
--------------
gate_open = ‘0’
counter == N-1 && car_entering == 1 && car_exiting == 0
car_exiting == 1
rst

## Slide 30: FSM: Top Level and Signal Declarations
module parking_lot ( input logic clk, input logic rst, input logic car_entering, input logic car_exiting, output logic gate_open ;( parameter N = 32'd10; // Signal declarations typedef enum { open_st, closed_st } sm_type; sm_type current_state; sm_type next_state; logic [31:0] counter; ... endmodule

## Slide 31: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= open_st; end else begin current_state <= next_state; end end

## Slide 32: FSM – Async Logic
always_comb begin next_state = current_state; case (current_state) open_st: begin gate_open = 1'b1; if ((counter == N - 1) && (car_entering == 1'b1) && (car_exiting == 1'b0)) begin next_state = closed_st; end end closed_st: begin gate_open = 1'b0; if (car_exiting == 1'b1) begin next_state = open_st; end end endcase end
Default assignment

## Slide 33: FSM – Aiding Synchronous Procedural Block
always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin counter <= 32'd0; end else begin if ((car_entering == 1'b1) && (car_exiting == 1'b0) && (counter != N)) begin counter <= counter + 1; end else if ((car_entering == 1'b0) && (car_exiting == 1'b1) && (counter != 32'd0) begin counter <= counter - 1; end end end
FA (Full Adder)
FS (Full Subtractor)

## Slide 34: FSM - summary
Before writing code – design
Divide into two procedural blocks
Define states with meaningful names
Every signal (wire) in always_comb must have:
  An assignment in all possible branches, or
  Default assignment

## Slide 35: How to Debug a FSM?
Always add the current and next state to the waveform
Given the current state and the inputs, check that the next state and output are as expected
As always, search for ‘x’ and ‘z’ values and ensure they make sense

## Slide 36: Wet Exercise 2
You will be required to:
  Design and implement a FSM
  Simulate it
  Use the behavioral model and not just logic gates
  Assembly coding: not learned in the workshops. Use tutorials.
In this exercise, there are no propagation delays!
The workshops cover all the syntax needed to solve the wet exercises

## Slide 37: Question 1
module simple_fsm (
output logic z,
input logic clk,
input logic rst,
input logic x
;(
typedef enum {S0, S1E, S1O, S2E, S2O} sm_type;
sm_type current, next;
// Next state sampling
always_ff @(posedge clk, posedge rst) begin
if (rst) begin
current <= S0;
end
else begin
current <= next;
end
end
// State Machine Outputs
always_comb begin
z = 1'b0;
case (current)
S2E: z = 1'b1;
endcase
end
// State transitions
always_comb begin
next = S0;
case (current)
S0: if (x == 1'b1) begin
next = S1O;
end
else begin
next = S1E;
end
S1E: if (x == 1'b1) begin
next = S2O;
end
else begin
next = S2E;
end
S1O: if (x == 1'b1) begin
next = S2E;
end
else begin
next = S2O;
end
endcase
end

## Slide 38: Question 2
module my_module(
input logic [1:0] w,
input logic a,
output logic z1,
output logic z2
);
always_comb begin
if (a == 1'b1) begin
z1 = ~a;
end
end
always_comb begin
z2 = 1'b1;
case (w)
2'b00: z2 = 1'b0;
2'b01: z2 = 1'b1;
2'b10: z2 = 1'b0;
endcase
end
endmodule
נתון הקוד הבא:

## Slide 39: Questions?