## Slide 1: SystemVerilog HDL Workshop #5
044252 - Digital Systems and Computer Structure

## Slide 2: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 3: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 4: Reminder – What is FSM?

## Slide 5: FSM – Writing Code
Declare states used for FSM
Write FSM using two procedural blocks:
  Synchronous – saves current state
  Asynchronous – sets next state and output signals (according to current state and optionally input signals)
Other helper procedural blocks can also be used

## Slide 6: FSM Template
module my_FSM_module (
input logic input1,
...
output logic outputN
;(
// Declaring the FSM states
typedef enum { idle_st, start_st } sm_type;
// Declaring signals for the next & current state
sm_type current_state;
sm_type next_state;
// ...
endmodule

## Slide 7: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 8: FSM – Async Logic
always_comb begin
next_state = current_state;
output1 = 1'b0;
...
outputN = 1'b0;
case (current_state)
idle_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
start_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
...
endcase
end
Default Assignments

## Slide 9: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 10: Control and Datapath Separation
Signals are classified into two categories:
  Data
    Usually buses (wide vectors)
    Common units: FAs, mux, ALU, …
  Control
    Usually single bits
    Common units: FSM
Data Processor
Controller
Data In
Data Out
Control
Status
External Status
External Control

## Slide 11: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 12: תקשורת על חוט יחיד
חוט טלפון, רשת מקומית, ...
במקום חוטי REQ, ACK:
  נשתמש בשעון איטי הרבה יותר מהשעונים הפועלים בשני הקצוות
  נסנכרן אותם מידי פעם:
גם זו קרויה "תקשורת אסינכרונית" אבל בעצם היא קצת סינכרונית
פרוטוקול תקשורת UART: Universal (Synchronous) Asynchronous Receiver/Transmitter
נהוג ביציאת COM של ה-PC
אפשרות אחרת (נהוגה ברשת מקומית מהירה): נקודד את השעון יחד עם הנתונים, למשל “Manchester Code”

## Slide 13: UART – Transmitter FSM

## Slide 14: Agenda
FSM – reminder
UART – reminder
Summarizing example

## Slide 15: UART3 Protocol
In this workshop, we will plan a UART transmitter with a few minor changes:
  3-bit word instead of an 8-bit word
  Sends a parity bit
stop | stop | stop | parity | parity | parity | bit3 | bit3 | bit3 | bit2 | bit2 | bit2 | bit1 | bit1 | bit1 | start | start | start
baud time
Tx transmitter

## Slide 16: Summarizing Example: UART3

## Slide 17: Top Level and Signal Declarations
module UART3 (
input logic clk,
input logic rst,
input logic [2:0] A,
input logic start,
output logic out
;(
parameter N = 3;
logic counter_done;
logic counter_clear;
logic [1:0] A_sel;
logic [1:0] out_sel;
logic parity_clr;
logic parity_enable;
UART3_fsm fsm_u(
.clk(clk),
.rst(rst),
.start(start),
.counter_done(counter_done),
.counter_clear(counter_clear),
.A_sel(A_sel),
.out_sel(out_sel),
.parity_clr(parity_clr),
.parity_enable(parity_enable)
;(
UART3_counter #(
.N(N)
) cnt_u (
.clk(clk),
.rst(rst),
.counter_clear(counter_clear),
.counter_done(counter_done)
;(
UART3_arith arith_u(
.clk(clk),
.rst(rst),
.A(A),
.A_sel(A_sel),
.out_sel(out_sel),
.parity_clr(parity_clr),
.parity_enable(parity_enable),
.out(out)
);
endmodule

## Slide 18: Simulations – Top Level
start
A[0]
A[1]
A[2]
parity
stop

## Slide 19: Building the FSM
Build a Mealy FSM
Requirements:
  Receives several signals:
    clk
    rst (asynchronous)
    start
    counter_done
  Outputs:
    parity_clr
    parity_enable
    A_sel
    out_sel
    counter_clr

## Slide 20: UART3: FSM Design
start == 1 /
parity_clr=1
rst
Start bit
Idle
First bit
Second bit
Third bit
Parity
counter_done && start == 0
counter_done && start == 1 /
parity_clr=1
Start == 0
Stop bit
Defaults:
parity_clr = 0
A_sel = 0
out_sel = 2
counter_clr = 1
parity_enable = 0
!counter_done /
counter_clr=0
out_sel=1
counter_done /
out_sel=1
!counter_done /
counter_clr=0
out_sel=0
counter_done /
parity_enable=1
out_sel=0
!counter_done /
counter_clr=0
out_sel=0
A_sel=1
counter_done /
parity_enable=1
out_sel=0
A_sel=1
!counter_done /
counter_clr=0
out_sel=0
A_sel=2
counter_done /
parity_enable=1
out_sel=0
A_sel=2
!counter_done /
counter_clr=0
out_sel=3
counter_done /
out_sel=3
!counter_done /
counter_clr=0

## Slide 21: FSM
module UART3_fsm ( input logic clk, input logic rst, input logic start, input logic counter_done, output logic counter_clear, output logic [1:0] A_sel, output logic [1:0] out_sel, output logic parity_clr, output logic parity_enable ); typedef enum { idle_st, start_bit_st, first_bit_st, second_bit_st, third_bit_st, parity_st, stop_bit_st } sm_type; sm_type current_state; sm_type next_state;

## Slide 22: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 23: FSM – Async Logic
always_comb begin next_state = current_state; parity_clr = 1'b0; A_sel = 2'd0; out_sel = 2'd2; counter_clear = 1'b1; parity_enable = 1'b0; case (current_state) idle_st: begin if (start == 1'b1) begin next_state = start_bit_st; parity_clr = 1'b1; end end start_bit_st: begin out_sel = 2'd1; if (counter_done) begin next_state = first_bit_st; end else begin counter_clear = 1'b0; end end
first_bit_st: begin out_sel = 2'd0; if (counter_done) begin next_state = second_bit_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end second_bit_st: begin out_sel = 2'd0; A_sel = 2'd1; if (counter_done) begin next_state = third_bit_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end

## Slide 24: FSM – Async Logic
third_bit_st: begin out_sel = 2'd0; A_sel = 2'd2; if (counter_done) begin next_state = parity_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end parity_st: begin out_sel = 2'd3; if (counter_done) begin next_state = stop_bit_st; end else begin counter_clear = 1'b0; end end
stop_bit_st: begin if (counter_done) begin if (start == 1'b0) begin next_state = idle_st; end else begin next_state = start_bit_st; parity_clr = 1'b1; end end else begin counter_clear = 1'b0; end end

## Slide 25: Simulations – FSM

## Slide 26: Arithmetic Unit
module UART3_arith (
input logic clk,
input logic rst,
input logic [2:0] A,
input logic [1:0] A_sel,
input logic [1:0] out_sel,
input logic parity_clr,
input logic parity_enable,
output logic out
);
logic parity;
logic A_out;
// A mux
always_comb begin
case (A_sel)
2'd0: A_out = A[0];
2'd1: A_out = A[1];
2'd2: A_out = A[2];
default: A_out = 1'b0;
endcase
end
// Out mux
always_comb begin
case (out_sel)
2'd0: out = A_out;
2'd1: out = 1'b0;
2'd2: out = 1'b1;
2'd3: out = parity;
default: out = 1'b0; // For simulation only
endcase
end
// Parity register
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
parity <= 1'b0;
end
else begin
if (parity_clr == 1'b1) begin
parity <= 1'b0;
end
else if (parity_enable == 1'b1)
begin
parity <= parity ^ A_out;
end
end
end
endmodule

## Slide 27: Simulations – Parity

## Slide 28: Counter
module UART3_counter (
input logic clk,
input logic rst,
input logic counter_clear,
output logic counter_done
);
parameter N = 3;
logic [31:0] counter;
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
counter <= 32'd0;
end
else begin
if (counter_clear == 1'b1) begin
counter <= 32'd0;
end
else if (counter < N - 1) begin
counter <= counter + 1;
end
end
end
always_comb begin
if (counter == N - 1) begin
counter_done = 1'b1;
end
else begin
counter_done = 1'b0;
end
end
endmodule

## Slide 29: Simulations – Counter

## Slide 30: Test Bench
module UART3_test; logic clk; logic rst; logic [2:0] A; logic start; logic out; UART3 #(.N(3)) uart ( .clk(clk), .rst(rst), .A(A), .start(start), .out(out) ;( initial begin clk = 1'b0; 5# rst = 1'b1; 10# rst = 1'b0; A = 3'b110; start = 1'b1; end always begin 5# clk = ~clk; end endmodule

## Slide 31: The Full Code
UART3_fsm fsm_u (…);
UART3_counter counter_u(…);
UART3_arith arith_u(…);
The full code is supplied with the workshop files
UART3.sv
UART3_fsm.sv
UART3_counter.sv
UART3_arith.sv
UART3_test.sv
UART3 uart3 (…);

## Slide 32: Debugging Tips Video
Hardware debugging is different than software debugging
  Waveform vs. tests / debug prints
The workshop code is supplied with a video which explains about debugging hardware
  Common mistakes
  How to track bugs using a waveform

## Slide 33: Exam Question
module mymodule2 (
input logic clk,
input logic rst,
output logic out
;(
logic w1;
logic w2;
mymodule uut1 (clk, rst, w1);
mymodule #(.N(2)) uut2 (clk, rst, w2);
always_comb begin
if ((w1 == 1'b1) && (w2 == 1'b1)) begin
out = 1'b1;
end
else begin
out = 1'b0;
end
end
endmodule
After reset, how many clock cycles are between two rises of out signal?

## Slide 34: Exam Question
module mymodule (
input logic clk,
input logic rst,
output logic done
;(
parameter N = 3;
logic [31:0] w;
always_ff @(posedge clk, posedge rst)
begin
if (rst == 1'b1) begin
w <= 32'd0;
end
else begin
if (w < N - 1) begin
w <= w + 1;
end
else if (w == N - 1) begin
w <= 0;
end
end
end
always_comb begin
if (w == N - 1)
begin
done = 1'b1;
end
else begin
done = 1'b0;
end
end
endmodule

## Slide 35: The Exam
One multiple-choice question (~5 points)
Questions from previous exams are partially irrelevant (Verilog/VHDL)
  Preparation questions are in Moodle
The material from the workshops and wet exercises is important. Implementation details from the wet exercises are not!
We are available for questions in the Moodle forum

## Slide 36: Questions?